## Slide 1: Evolving the End-to-End Transport Layer in Times of Emerging Computing In The Network (COIN)
Ike Kunze*, Dirk Trossen#, Klaus Wehrle*
* RWTH Aachen University # Huawei
1st Workshop on New IP and Beyond, October 2022

## Slide 2: Computing In The Network – From Dumb to Smart Networks
Host A
Host B
End-to-end principle
  Network as a dumb pipe
  Basis for transport protocols
COIN
  Network no longer a dumb pipe
  Breaks transport layer assumptions[1]
What does it take to have a COIN-enabled transport?
[1] Stephens et al.: TCP is Harmful to In-Network Computing: Designing a Message Transport Protocol (MTP), HotNets ‘21

## Slide 3: End-to-End Argument
Seminal work by Saltzer et al.[2]
  “The function […] can completely and correctly be implemented only with the knowledge […] of the application […] at the endpoints […].”
    Seemingly at odds with COIN
  “[…] an incomplete version of the function provided by the communication system may be useful as a performance enhancement.)”
    Aligns COIN with the end-to-end argument
Two critical aspects
[2] Saltzer et al.: End-To-End Arguments in System Design, ACM TOCS, vol. 2, no. 4, 1984
  Location
  Which computation?

## Slide 4: COIN – Compute Locations
Host A
Host B
COIN compute locations
  Strict (only networking devices) to lax (subset of edge/cloud computing)
  Abstraction: COIN element
Location in relation to the endpoints
  On-path vs. off-path
Off-path COIN element
On-path COIN elements

## Slide 5: COIN – What kind of functionality?
Host A
Host B
F={f0, f1, f2, ... fn}
f1‘
G
E2E-function-internal
E2E-function-external
Not COIN!
E2E-function-internal computation on on- & off-path COIN elements
How and where to place functionality?

## Slide 6: First Design Principle for COIN
Host A
Host B
First COIN Design Principle
  Adhere to the original requirements of the E2E function,
  Enrich its functionality
  Optimize functional complexity against its key communication requirement
Simplicity Principle[3]
  “[…] we must drive our architectures and designs toward the simplest possible solutions.”
[3] Bush and Meyer: RFC 3439
f1’
f1’’

## Slide 7: Second Design Principle for COIN
Missing transparency might lead to problems
Second COIN Design Principle
  Insert in full transparency to the endpoints
Host A
Host B
f1’
F={f0, f1, f2, ... fn}

## Slide 8: Considerations for Transport
Functionality traditionally implemented in endpoints only
Directly impacted by emerging COIN capabilities
Several aspects to consider
Adressing
Flow Granularity
Collective Communication
More details
More aspects

## Slide 9: Transport Addressing
Host A
Host B
Host B
Implicit integration
  Hard to maintain
  Only on-path notion
Explicit steering
  Explicitly address
  How to do the addressing?
?
f1’
f1’
f1’
f1’

## Slide 10: Transport Addressing
Host A
Host B
Instance selection
  Multiple possible locations
  How to select them?
    Specify constraints?
    Specify locator?
Affinity
  Might be needed
  How to realize that?
    Setup during “orchestration”?
    Route based on service identifier?
f1’
f1’
f1’
upper

## Slide 11: Existing Solutions & The Way Ahead
Transport Addressing
  Source routing
    Only which path not which functionality
  Service function chaining
    Steer traffic through functions
  Information centric networking
    Address information rather than endpoints
Many open questions
Main takeaway: COIN can align with end-to-end principle

## Slide 12: Conclusion
COIN seemingly at odds with end-to-end principle
E2E-function-internal COIN computations align
  On- vs. off-path COIN elements
Two design principles for COIN
Transport considerations
Paper
Draft